## Slide 1: PRESENTATION TITLE
Lecture 12: Gated Latch and D Latch Design
EGEC 180 – Digital Logic and Computer Structures
Spring 2024
Rakesh Mahto, Ph.D.
Office: E 314, California State University, Fullerton
Office Hour: Monday and Wednesday 2:00 - 3:30 pm
Or by appointment
Office Hour Zoom Meeting ID: 891 2907 5346
Email: ramahto@fullerton.edu
Phone No: 657-278-7274

## Slide 2
Gated Latch and D Latch Design

## Slide 3: Gated Latch
A gated latch circuit can be created by adding a control input C to an S-R latch circuit.
The control input is used to retain or hold the present-state output value.
A gated latch circuit is level sensitive (output depends on logic level at input).
With S-R NOR Latch
C = 0 implies hold
With S-R NAND Latch
C = 1 implies hold
Logic Symbol
Notes: Homework 1 was due last Thursday, so students still have until this Thursday to get credit with a late penalty.

## Slide 4
D Latch Circuit Design with S-R Latches
With S-R NOR Latch
With S-R NAND Latch
D Latch or DATA Latch
Logic Symbol
With NOT gate S cannot be equal to R.

## Slide 5
Characteristic Table for D Latch
If C = 1 then Q+ = D
PS/NS Table
Notes: present state/next state

## Slide 6
Reduced AND/OR Circuit for a D Latch
Q+ = C’Q + CD
Q+ = C’Q + CD; C = A
2-to-1 MUX Equation: Z (output) = A′I0 + AI1
A is select line, I0 and I1 are input lines.

## Slide 7
Setup-Time and Hold-Time
Setup-Time, tsu: Required time before a clock pulse that an input signal must be settled
Hold-Time, th: Required time after a clock pulse that an input signal must remain settled
Sampling-Interval, tsi: Setup-Time + Hold-Time
Metastable State: Indeterminate value, not a stable 0 or 1

## Slide 8
Timing Diagram for a D Latch
Observe: Setup-time violation, Hold-time violation, Logic 0 glitch, and Metastable state
To avoid circuit malfunction D must be constant during the entire sampling interval tsi

## Slide 9
Setup-Time and Hold-Time
Setup-time violation can be fixed simply by slowing down the clock
How can one fix a Setup-Time and Hold-Time violation?
Hold-time violation can be fixed by adding delay before the input. Can’t be fixed after fabrication (chip-killer)!

## Slide 10
Flip-Flops

## Slide 11
Edge-Triggered D Flip-Flop
A D flip-flop has two inputs, D (data) and Ck (clock). The small arrowhead on the flip-flop symbol identifies the clock input. Unlike the D latch, the flip-flop output changes only in response to the clock, not to a change in D.
If the output can change in response to a 0 to 1 transition on the clock input, we say that the flip-flop is triggered on the rising edge (or positive edge) of the clock.
If the output can change in response to a 1 to 0 transition of the clock input, we say that the flip-flop is triggered on the falling edge (or negative edge) of the clock. An inversion bubble on the clock input indicates a falling-edge trigger.

## Slide 12: D Flip-Flops
Write back
Write back
Write back
Write back
D
Q
D
Q
Positive Edge Triggered FF
Negative Edge Triggered FF

## Slide 13: D Flip-Flops
Q = D
+

## Slide 14
Positive Edge-Triggered D Flip-Flop with CLR Input
A Flip-Flop is specifically designed so that its output will not break into oscillations when feedback is added externally around it because it is edge triggered, as opposed to the D Latch which is level sensitive.
Master-Slave D FF: no transparent or see-through mode.

## Slide 15
Manual K-Map Reduction for Q+
Consensus term removes the logic glitch: DQ.

## Slide 16
D Latch with a CLR Input: a) implemented with a logic hazard-free function in AND-OR circuit form, and b) logic symbol
Extra term removes the logic glitch: C’Q + CD + DQ

## Slide 17
Annotated Gate Level Circuit for a Positive Edge-Triggered D FF with a CLR Input Implemented with Three S-R NAND Latches and a NOT Gate

## Slide 18
Timing Diagram for a Positive Edge-Triggered D FF

## Slide 19
Logic Symbol for a Standard D Flip-Flop:
CLR is an asynchronous signal for CLEARING (CLR)
PRE is an asynchronous signal for SETTING
CLR or Reset (RST) and PRE or Set (SET) are active high; logic 1
Asynchronous implies clock (CLK) independent

## Slide 20
Simulation for the DFF Design
Note: raising edge of clock is when Q changes.
RST = 1 D and Q are 0

## Slide 21: Q&A